## Slide 1
PN Junction Diode: The Basics
The PN junction diode is a fundamental electronic device. It controls current flow in circuits. Silicon and Germanium are common semiconductor materials. Diodes are used in rectifiers, signal processing, and LEDs.
B. Priyal
24bd1a26687
CSM -E

## Slide 2
Semiconductors: Intrinsic Materials
Silicon Structure
Each silicon atom bonds covalently with four neighbors.
Intrinsic Silicon
Pure silicon with equal electrons and holes.
Electrical Properties
Limited conductivity at room temperature due to low carrier density.

## Slide 3
Doping: Creating N-Type Semiconductor
What is Doping?
Adding impurities to change electrical behavior of semiconductors.
N-Type Semiconductor
Doped with pentavalent elements like phosphorus.
Extra free electrons
Electron concentration from 10¹⁵ to 10¹⁹ atoms/cm³
Increased conductivity

## Slide 4
Doping: Creating P-Type Semiconductor
P-Type Semiconductor
Doped with trivalent impurities such as boron and gallium.
Holes as Carriers
Electron vacancies act as positive charge carriers increasing conductivity.
Hole Concentration
Ranges from 10¹⁵ to 10¹⁹ atoms/cm³.

## Slide 5
The PN Junction Formation
Formation Process
P-type and N-type materials joined together form the PN junction.
Carrier Diffusion
Electrons diffuse from N to P side
Holes diffuse from P to N side
Recombination neutralizes carriers near the junction.

## Slide 6
Depletion Region
Carrier-Free Zone
The depletion region lacks free charge carriers.
Electric Field
Created by ionized donor and acceptor atoms.
Barrier Potential & Width
Voltage: 0.7V for silicon, width ~0.5-1 µm.

## Slide 7
Forward Bias
1
Connecting Voltages
Positive to P-side, negative to N-side.
2
Depletion Region Narrows
Current can now flow through the diode easily.
3
Turn-On Voltage
Starts significant conduction at ~0.7V for silicon.
4
Exponential Current Increase
Current rises exponentially with applied voltage.

## Slide 8
Reverse Bias
Voltage Polarity
Negative to P-side, positive to N-side.
Depletion Region Widens
Current flow is effectively blocked.
Reverse Saturation Current
Small leakage due to minority carriers.
Breakdown Voltage
Voltage at which diode conducts in reverse direction.

## Slide 9
Diode Characteristics Curve
Forward Region
Current rises exponentially after turn-on voltage.
Reverse Region
Small leakage current until breakdown voltage.
Temperature Effects
Leakage current increases, forward voltage drop decreases.

## Slide 10
Applications of PN Junction Diodes
Rectifiers
Convert AC to DC power.
Signal Diodes
Handle small signals in circuits.
LEDs
Emit light when forward biased.
Voltage Regulation
Zener diodes control voltage levels.
Solar Cells
Convert light energy to electricity.